## Slide 1: LPC-10 Speech Encoder Implementation
December 16, 2020
Karndeep Singh Rai-Bhatti

## Slide 2: Motivation
Speech compression for communication systems
  Telephones
  Voice over IP
  Videoconferencing
Maximize audio data compression
  Without corrupting the words being spoken
  Retaining an intelligible voice
  Additional Security - encryption
Model that Emulates Human Speech Generation – Physical Model

## Slide 3: Physical Model of Speech and Synthesis
Air ~ Speech volume
  Gain
Vocal Cords ~ Excitation signal
  Impulse train
  Period = fundamental Frequency of voice
Vocal Tract ~ Linear Transformation
  Modeled by All Pole System
  Our Linear Predictor
Speech ~ Output signal
  Pass excitation through filter with appr

## Slide 4: Modeling Speech as a LTI system
Model holds true at small intervals (25ms)
Unvoiced is approximated as 4th order all-pole filter
Voiced is approximated as 10th order all-pole filter

## Slide 5: LPC-10 workflow
Signal
Pre-Emphasis Filter
High pass
LCP Analysis
Gain, Pitch, and Voice Analysis
All Pole Coefficients
Gain, Pitch and Voicing
Parameter Coding
ENCODER
Pitch, Voicing
Excitation Generator
Sythesizer
Gain
Reconstruction
DENCODER
Parameters
(Gain, Pitch, Voicing, Coefficients)
All Pole Coefficients
Impulse train

## Slide 6: What did I do?
Implemented LPC-10
  Look at system holds up to different users and emotions
Attempted to Improve LPC-10
  Voiced detection
  All-Pole Filter
  Pitch Interpolation
  Gain Interpolation
Implemented LPC-10 in real-time using MATLAB

## Slide 7: Data Set: EmoV-DB
Databased for characterizing how Emotionally Expressive a Voice Generation System is
4 Speakers
  Bea & Jenie (female)
  Sam & Josh (male)
  All Bea data recorded at 44k, so it was excluded
5 emotions
  Neutral, Sleepiness, Anger, Disgust, Amusement
  We will look at Neutral, Anger, Sleepiness
Use to assess the quality of our LPC-10 Reconstruction
https://github.com/numediart/EmoV-DB

## Slide 8: Emotions and Signal Periodicity
Emotions tied to periodicity of speech signal
Anger/Strong Emotions: Expect More Periodicity
  Expection: Ideal case for model
Fatique/Weak Emotions: Speech becomes more Aperiodic
  Expectation: Model will perform more poorly
LPC-10 relies on the assumption that speech is periodic at small time scales (ms)
Test the robustness of the algorithm

## Slide 9: Angry Audio – LPC10
Periodic Signal
Waveforms matched closely
Audio suffers from distortion, primarily when volume peaks
Sam

## Slide 10: Neutral Audio – LPC10
Appears to work a lot better on female voices
Cadence of Voice significant factor in clarity
Reduced distortion compared to Angry speech

## Slide 11: Sleepy Audio – LPC10
Non-vocal noises handled poorly (high frequency jitter)
  Reconstruction is very ‘Breathy’
Slow speech significantly easier to understand

## Slide 12: Limitation of LPC?
Distortion – failed prediction
Voiced Determination? (all prior used zero crossing)
Increase number of coefficients?

## Slide 13: Voiced Detection – Energy vs Zero-Crossing
Energy Based Approach
  For a speech clip:
    Absolute value ()
    Summation ()
    Normalize to clip length
  If energy > energy Threshold
    Speech
  Else
    Noise
Tests Energy or Volume
Zero-Crossing
  For a speech clip:
    Turn in 1s -1s depending on sign
    Take derivative
    Count number of flips (zero-crossings)
    Normalize to length of clip
  If # zero crossings > crossing Threshold
    Noise
  Else
    Speech
Test Periodicity
Notes: Noise clip will constantly meet this metric

## Slide 14: Voiced Detection – Jenie-Sleepy
Energy Based Approach
  Better preserve of Pitch
Zero-Crossing
  Less noise/artifacts

## Slide 15: Coefficient Estimation – Number Coefficients
N = 10
  Used in official Standard
Tested on very clear sample
  N = 5
  N = 20
  N = 40
Test using both Voicing methods

## Slide 16: Coefficient Estimation – Number Coefficients
Energy Based Voice
N = 5
N = 10
N = 20
N = 40
Zero Crossing Based Voice
N = 5
N = 10
N = 20
N = 40
Significant increase in quality for both!

## Slide 17: Coefficient Estimation – Re-visit Sleepy Jenie
LPC n = 10
  From Before
LPC n = 40
  Subjectively better, later portion
Notes: Up to this point: We can see increased number of coefs does wonders and how sound made by the two different voiced algorithm appears

## Slide 18: Improvements to LPC-10: Interpolation

## Slide 19: Pitch linear interpolation
Pitch calculated on a window to window (200 samples)
Idea: Linearly interpolate period from prior window
Problem: Signal Period is Large Relative to windows
Shift correction

## Slide 20: Pitch linear interpolation - Results
Pitch interpolation – Clearer?
Shift correction reduced some artifacts
Note: Some past data has the shift correction.
Also Tried on Sleepy Sam:
Without With

## Slide 21: Gain Interpolation
Apply an envelope to signal
Linearly Interpreting gains of each bin
Reduces Artifacts
Pitch interpolation only:

## Slide 22: Real Time LPC demo
Compare different filter orders
Has shift correction implemented
There may be a significant delay in speech

## Slide 23: Work Cited
Spanias, A. (1994). Speech Coding: A Tutorial Review. Proceedings of the IEEE, 82(10), 1541-1582. https://doi.org/10.1109/5.326413
Kang, G., & Everett, S. (1985). Improvement of the excitation source in the narrow-band linear prediction vocoder. IEEE Trans. Acoust. Speech Signal Process., 33, 377-386.